Development of Standard Produk Data Processing and Receiving Ground Station System For Earth Resources Remote Sensing Satellite LDCM (Landsat Data Continuity Mission)

Pengembangan Sistem Stasiun Bumi Penerimaam dan Pengolahan Produk Standard Data Satelit Penginderaan Jauh Sumber Daya Alam LDCM (Landsat Data Continuity Mission)

Hidayat Gunawan, Ali Syahputra Nasution, Dinari Niken SS  dan  Ayom Widipaminto *)

*) Perekayasa Bidang Teknologi Akusisi dan Stasiun Bumi Penginderaan Jauh,

Lembaga Penerbangan dan Antariksa Nasional,

Jl. LAPAN No. 70 Pekayon, Pasar Rebo, Jakarta Timur 13710, Indonesia

Telp/Fax. +62 21 87717816

E-mail : hgun@lapan.go.id,  hgun1708@yahoo.com and ayomwidi@yahoo.com

Abstract

In order to maintain continuity of national natural resources of satellite remote sensing data, Remote Sensing Deputy of LAPAN needs to prepare infrastructure to be able to receive, record, and process the LDCM satellite remote sensing data. LDCM satellite sensing (Landsat Data Continuity Mission) is a continuation series of Landsat satellites earlier and have been launched in March 2013. To support the LDCM satellite data reception and procssing preparation activities, the study and development of LDCM satellite data receiving and processing need to be done. In previous activities have been conducted studies upgrading LAPAN Earth Station  for the LDCM. In this paper will be carry out the implementation of concept, requirement and specifications of hardware and software of Landsat satellite data processing and reveiving system  to develop  LDCM data processing and receiving system in LAPAN.

LDCM satellite carried two sensors namely Operational Land Imager (OLI) and Thermal Infrared Sensors (TIRS). The second mission sensor data will be bundled in real time and playback to the receiving earth station satellite data LDCM. Mission of real-time data and playback will be sent to the earth station is assembled in the Ground Network Element (GNE) and real-time data will be transmitted to ground stations are assembled in the International Cooperator (IC). LDCM satellite data Receiving ground station system consists of radio frequency subsystem  (RF), demodulator and Data Collection and Routing System (DCRS) which perform data acquisition up to the satellite mission data archiving. While the standard product processing system includes a data processing subsystem Ingest mission into the level-0 data and Landsat Product Generation sytem (LPGS) which processing data into a data level-0 level-1 standard products.

Developted sistem have been successfully for LDCM satelit signal receiving on Mei 2013, and have been successfully for LDCM mission data processing on Juni 2013. For the next step the system will be upgrade for LDCM data receiving and processing operation. This Development  of LDCM data processing and receiving sistem have been carry out to upgrade Landsat/LDCM standard product data processing and receiving system in LAPAN in order to support National Remote Sensing Data Bank Programs.

Keywords: Receiving System, RF-DCRS, Processing Systems, Ingest-LPGS, Landsat Data Continuity Mission (LDCM)

Abstrak

Dalam rangka menjaga kontinuitas data satelit penginderaan jauh sumber daya alam nasional,  LAPAN dalam hal ini kedeputian penginderaan jauh perlu mempersiapkan infrastrukturnya untuk mampu menerima, merekam, dan mengolah data satelit penginderaan jauh LDCM. Satelit Inderaja LDCM (Landsat Data Continuity Mission) merupakan seri kelanjutan satelit Landsat sebelumnya dan sudah diluncurkan pada bulan Maret 2013. Untuk mendukung kegiatan penerimaan dan pengolahan data satelit LDCM, perlu dilakukan kajian dan pengembanngan sistem penerimaan dan pengolahan data satelit LDCM. Pada kegiatan sebelumnya telah dilakukan kajian upgrading Stasiun Bumi LAPAN, selanjutnya dalam makalah ini akan diimplementasikan hasil kajian konsep, requirement dan spesifikasi hardware dan software sistem penerima dan pengolahan data satelit LDCM, dalam rangka pengembangan dan rancangbangun sistem penerima dan pengolahan data satellite LDCM (Landsat Data Continuiti Mission) di LAPAN

Satelit LDCM  mempunyai dua sensor yaitu Operational Land Imager (OLI) dan Thermal Infrared Sensor (TIRS). Data misi kedua sensor tersebut akan dipaketkan secara real time dan playback ke stasiun bumi penerima data satelit LDCM. Data misi real-time dan playback akan dikirimkan ke stasiun bumi yang terhimpun dalam Ground Network Element (GNE) dan data real-time saja akan dikirimkan ke stasiun bumi yang terhimpun dalam International Cooperator (IC). Sistem stasiun bumi penerima data satelit LDCM terdiri dari subsistem Radio Frequensi (RF), demodulator dan Data Collection and Routing System (DCRS) yang melakukan akusisi data satelit sampai dengan pengarsipan data mission. Sedangkan sistem pengolahan produk standar meliputi subsistem Ingest yang mengolah data mission menjadi data level-0 dan Landsat Produk Generation Sytem (LPGS) yang mengolah data level-0 menjadi data produk standar level-1.

Sistem yg dibangun sudah bisa dilakukan penerimaan test downlink signal satelit LDCM pada bulan Mei 2013, sedangkan test uji coba pengolahan sudah berhasil dilakukan sejak bulan Juni 2013, dan diharapkan mulai bulan Juli 2013 sistem penerimaan dan pengolahan data satelit LDCM bisa ditingkatkan menjadi operasional. Pengembangan dan rancang bangun sistem penerima dan pengolah data satelit LDCM dilakukan untuk upgrading sistem penerimaan dan pengolahan produk standar data satelit LDCM di LAPAN dalam rangka mendukung program  Bank Data Penginderaan Jauh Nasional.

Kata Kunci: Sistem Penerimaan, RF-DCRS, Sistem Pengolahan, Ingest-LPGS, Landsat Data Continuity Mission (LDCM)

Note:

Abstrak ini merupakan revisi dari abstrak yang sudah dikirim sebelumnya pada bulan Mei 2013, dengan update status pengembangan kegiatan litbang terkini di LAPAN.

Mohon bisa dijadikan maklum

Terimakasih

Penulis