Identifying Natural Revegetation of Mine Waste

Using Compact Polarimetry

Bambang H. Trisasongko1, David J. Paull2, Dyah R. Panuju1

1Department of Soil Science and Land Resources, Bogor Agricultural University,

Jalan Meranti, Bogor 16680, Indonesia. Email: trisasongko@live.it

2School of Physical, Environmental and Mathematical Sciences, UNSW Canberra,

Northcott Drive, Canberra 2600, Australia.

Abstract: Mining waste poses a considerable a threat to surrounding environments. Great effort must, therefore, be made to monitor and rehabilitate broad zones where mine tailings are depositied. This paper presents an approach to observe natural revegetation on a tailings deposition zone using C-band fully polarimetric Synthetic Aperture Radar (PolSAR). Since PolSAR acquisition generally consumes high energy, we evaluate the possibility of halving transmitted energy using compact polarimetry theorems. In this paper, three compact polarimetric techniques and three modes of reconstruction are studied to reconstruct PolSAR data and assessment is performed using Pauli decomposition. We conclude that compact polarimetry can be exploited to some extent. If PolSAR reconstruction is needed, this research demonstrates that the Polar State extrapolation generates a Covariance Matrix closely resembling the original PolSAR data. Natural forests are generally well recovered; however, it appears that reeds are slightly over estimated.

Keywords: Compact Polarimetry, Mine Waste, Pauli Decomposition, Reeds, Revegetation

Intended Topic: Method development and Image Processing - Synthetic-aperture radar (SAR) and Interferometric Synthetic Aperture Radar (InSAR) Processing or Microwave and LidarProccessing